## Slide 1
Scaling Qubit Readout with Hardware Efficient Machine Learning Architectures
ISCA - 50
Satvik Maurya (UW-Madison)
Chaithanya N. Mude (UW-Madison)
William D. Oliver (MIT)
Benjamin Lienhard (Princeton)
Swamit Tannu (UW-Madison)

## Slide 2: Qubit Readout
Qubits
DACs
ADCs
Qubit Readout
Qubit Control
FPGA/ASIC
Qubit Control: Manipulates the state of the qubits
Qubit Readout: Measures the state of the qubits (0/1)
WRITE
READ
Notes: Readout is a fundamental operation in quantum computing, it involves reading the state of a qubit by sensing a very small analog signal that is digitized by an ADC. Control is the reverse operation that writes a state onto a qubit.

## Slide 3: Readout Error Rates are High!
Chart: Worst-case Readout Error Rate
| ibmq_belem (16) | ibmq_quito (16) | ibmq_manila (32) | ibm_nairobi (32) | ibm_oslo (32) | ibm_algiers (128)
Error Rate | 2.72 | 7.2 | 3.5 | 10.93 | 14.44 | 25.05
Focus: Improving readout state classification.
Quantum Volume
Notes: Readout is the noisiest operation on current quantum computers as shown in this chart which plots the worst case readout error for different IBM quantum computers. Readout consists of many components and we will be focusing on the signal processing part which is state classification.

## Slide 4: Current State-of-the-Art Classifier
1Lienhard, Benjamin, et al. "Deep-neural-network discrimination of multiplexed superconducting-qubit states." Physical Review Applied 17.1 (2022): 014024.
Baseline1 Classifier Design
ADC
Qubit state classifier
0 to 31
Multiplexed readout
Signal
(5 qubits)
0/1
>½ million parameters!
Qubits
Readout signal
A state-dependent readout signal is acquired from the qubits that is digitized by an Analog-to-Digital Converter.
This digitized data is used for state classification.
ADC
1000 sample buffer
Time
dependent
signal
Notes: Before I present our proposed design, I’d like to talk about the current state of the art classifier and the advantages and disadvantages it offers.
Typical readout pipeline
Baseline design that uses all possible features of the readout signal by buffering the digitized samples and feeding them all to a very large neural network.

## Slide 5: Current State-of-the-Art Classifier
0 - 31
Multiplexed readout
Signal
(5 qubits)
>½ million parameters!
ADC
1000 sample buffer
Up to 25% reduction in state assignment error rate compared to contemporary classifiers.
Up to 10x reduction in readout crosstalk.
High hardware complexity (>100% LUT utilization on Xilinx MPSoCs)
But…..
Slow if implemented in software
Notes: The baseline design offers significant improvement in classification accuracy, and mitigation of readout crosstalk.
However, this classifier cannot be efficiently implemented on hardware, and will be very slow if implemented in software because of the overhead of transferring all the samples to software

## Slide 6: Control Hardware Must Be Scaled Too!
https://ai.googleblog.com/2023/02/suppressing-quantum-errors-by-scaling.html
~30 FPGAs
??? FPGAs
Number of FPGA scaling linearly with qubits is not sustainable
Notes: The reason we want classifiers and other components involved in qubit control and readout to scale well is because control hardware must be scaled along with the number of qubits.
This roadmap was published by google and IBM has a similar timeline for scaling their systems and if we consider the 54 qubit system that Google used for their supremacy experiment, the number of FPGAs needed was quite large. If we continue with the same linear scaling, the control hardware needed for 10000 qubits would be very costly and complex.

## Slide 7: Can we reduce the hardware complexity of the baseline classifier while retaining its benefits?
Notes: And so, the key question we wanted to answer was whether we could create a more scalable, hardware-efficient classifier that would still retain all the benefits of the state-of-the-art.

## Slide 8: Goal – Reduce Classifier Hardware Complexity
Retain crosstalk mitigation advantages offered by neural networks.
Reduce hardware complexity.
Readout Error
Classification latency /
Hardware complexity
IBM hardware classifier
Large FNN Classifier (baseline)
Hardware classifiers
Software classifiers
Notes: This slide also visualizes our goal. We want to decrease the readout error and decrease the latency and hardware complexity of the classifier.

## Slide 9: Visualizing Readout
ADC
Qubits
Inphase (I)
Quadrature (Q)
The readout signal is split into two channels – Inphase (I) and Quadrature (Q).
The readout signal is received from the qubits is a continuous time signal of duration > 100ns.
Notes: So how do we do this? We can start by visualizing the readout process.

## Slide 10: Visualizing Readout
ADC
Qubits
Inphase (I)
Quadrature (Q)
The readout signal is split into two channels – Inphase (I) and Quadrature (Q).
The readout signal is received from the qubits is a continuous time signal of duration > 100ns.

## Slide 11: Visualizing Readout
ADC
Qubits
I
Q
Filter
Classifier
Filtering reduces the dimension of the input signal – usually an averaging filter.
1000s of shots
(Ideal)
The readout signal is split into two channels – Inphase (I) and Quadrature (Q).
The readout signal is received from the qubits is a continuous time signal of duration > 100ns.

## Slide 12: Relaxations: Major Source of Readout Errors
Chart: Per Qubit Misclassifications
| Qubit 1 | Qubit 2 | Qubit 3 | Qubit 4 | Qubit 5
0 | 7.17 | 105.444 | 27.502 | 29.439 | 11.33
1 | 27.987 | 186.059 | 83.024 | 42.673 | 37.165
Qubits prepared in state ‘1’ relax back to the ground state during readout
(Reality)

## Slide 13: Detecting Relaxations

## Slide 14: Relaxations can be detected
Traces corresponding to relaxations are distinct  can be detected using template matching algorithms.

## Slide 15: Template Matching
Input
Template
Match /
No match
Template matching with matched filters
Template matching
Matched filter
Matched filter a.k.a.
Fisher’s Linear Discriminant

## Slide 16: Our Proposed Design - HERQULES
Readout
Signal
0 - 31
Use traces corresponding to relaxations for
training Relaxation Matched Filters (RMF).
parameters
MF
RMF
0 or 1?
True 0 or 10?
MF
RMF
NN

## Slide 17: Hardware Utilization
Chart: Resource utilization on a Xilinx MPSoC
| LUT | FF | BRAM | DSP
Baseline | 468.64 | 133.96 | 2.56 | 100
HERQULES | 7.79 | 0.75 | 2.56 | 1.85
If an FPGA large enough to fit the baseline is used, HERQULES can fit the hardware required for readout of >10x more qubits.
1Lienhard, Benjamin, et al. "Deep-neural-network discrimination of multiplexed superconducting-qubit states." Physical Review Applied 17.1 (2022): 014024.

## Slide 18: Readout Accuracy
 | Baseline1 | HERQULES
Qubit 1 | 0.969 | 0.985
Qubit 2 | 0.753 | 0.754
Qubit 3 | 0.943 | 0.966
Qubit 4 | 0.946 | 0.962
Qubit 5 | 0.97 | 0.989
Ƒ5Q | 0.9122 | 0.9266
1Lienhard, Benjamin, et al. "Deep-neural-network discrimination of multiplexed superconducting-qubit states." Physical Review Applied 17.1 (2022): 014024.
16% relative improvement

## Slide 19: Readout Crosstalk Mitigation
Design |  |  |  | 
Baseline1 | 0.002 | 0.005 | 0.002 | 0.0003
HERQULES | 0.0031 | 0.0062 | 0.0008 | 0.0005
Design |  |  |  | 
Baseline1 | 0.002 | 0.005 | 0.002 | 0.0003
HERQULES | 0.0031 | 0.0062 | 0.0008 | 0.0005
Cross-Fidelity  Lower is better
1Lienhard, Benjamin, et al. "Deep-neural-network discrimination of multiplexed superconducting-qubit states." Physical Review Applied 17.1 (2022): 014024.

## Slide 20: Enabling Faster Readout
HERQULES can achieve higher readout accuracy with
a shorter readout duration without requiring re-training.
1Lienhard, Benjamin, et al. "Deep-neural-network discrimination of multiplexed superconducting-qubit states." Physical Review Applied 17.1 (2022): 014024.
1
HERQULES

## Slide 21
Conclusions
Existing state-of-the-art classifiers expensive to implement on hardware.
We present a classifier that uses matched filters with a small, lightweight neural network to mitigate crosstalk that can be easily implemented on hardware.
Our proposed classifier achieves a 16.4% relative improvement in the combined state assignment accuracy.

## Slide 22: Questions?

## Slide 24
Backup

## Slide 25: Surface Code Simulations

## Slide 26: Matched Filters
Matched Filter (or Fisher’s linear discriminant): Optimal integration envelope to reduce data dimensionality and enable efficient qubit state discrimination
Envelope for single qubit:
⟨ground-state readout trace — excited-state readout trace⟩
var(ground-state readout trace — excited-state readout trace)

## Slide 27: Baseline Classifier

## Slide 28: HERQULES

## Slide 29: Accuracy
Design | Qubit 1 | Qubit 2 | Qubit 3 | Qubit 4 | Qubit 5 | F5Q | F4Q
Baseline1 | 0.969 | 0.753 | 0.943 | 0.946 | 0.97 | 0.912 | 0.957
MF | 0.968 | 0.734 | 0.891 | 0.934 | 0.956 | 0.892 | 0.937
MF-SVM | 0.968 | 0.738 | 0.895 | 0.928 | 0.953 | 0.892 | 0.936
MF-NN | 0.969 | 0.740 | 0.901 | 0.936 | 0.957 | 0.896 | 0.940
MF-RMF-SVM | 0.981 | 0.752 | 0.959 | 0.957 | 0.986 | 0.923 | 0.970
MF-RMF-NN | 0.985 | 0.754 | 0.966 | 0.962 | 0.989 | 0.927 | 0.975
1Lienhard, Benjamin, et al. "Deep-neural-network discrimination of multiplexed superconducting-qubit states." Physical Review Applied 17.1 (2022): 014024.

## Slide 30: Crosstalk Mitigation
Design |  |  |  | 
Baseline1 | 0.002 | 0.005 | 0.002 | 0.0003
MF | 0.0108 | 0.015 | 0.0021 | 0.0008
MF-NN | 0.0071 | 0.011 | 0.003 | 0.0003
MF-RMF-SVM | 0.011 | 0.0077 | 0.0024 | 0.0006
MF-RMF-NN | 0.0031 | 0.0062 | 0.0008 | 0.0005
Design |  |  |  | 
Baseline1 | 0.002 | 0.005 | 0.002 | 0.0003
MF | 0.0108 | 0.015 | 0.0021 | 0.0008
MF-NN | 0.0071 | 0.011 | 0.003 | 0.0003
MF-RMF-SVM | 0.011 | 0.0077 | 0.0024 | 0.0006
MF-RMF-NN | 0.0031 | 0.0062 | 0.0008 | 0.0005

## Slide 31: Noisy Simulations

## Slide 32: Training Curve

## Slide 33
Dream
(100,000 Qubits)
Current NISQ
(100+ Qubits)
Near Future NISQ
(1000 Qubits)
Mitigate Hardware Errors
Scale
Control Architecture
New Materials, Devices, …